## Slide 1: Speech Recognition
by
Prof. Alaa Hamdy

## Slide 2: Outlines
Sound, Audio, Music, Speech
Speech components (Speaker-related information, Speech)
Speech processing & speech analysis
Speech recognition (SR), Speaker identification, Speaker verification
Isolated-word & continuous SR
Difficulties of speech recognition
Sampling Theorem
Speech features (Zero-crossing, energy, power, formant, Fourier descriptor, Mel-frequency cepstral coefficients (MFCC), LPC, …)
Classification (HMM, ….)

## Slide 3: Sound Waves

## Slide 7: Sound, Audio, Music, Speech
Physical - sound as a disturbance in the air
  Amplitude
  Frequency
Audio (20 Hz  20,000 Hz)
Music (20 Hz  20,000 Hz)
Speech (300 Hz  3400 Hz)

## Slide 9: Speech Components
Speaker-related information
Speech information
Emotion information
Others

## Slide 10: Difference between image processing & analysis

## Slide 11: Difficulties of speech recognition
1. Environmental Interference
2. Linguistic Complexity
3. Speaker Diversity and Atypical Speech

## Slide 12: 1. Environmental Interference
Background Noise: Sudden loud noises, music, or wind degrade audio signals, making it difficult for the system to isolate the speaker's voice.
Microphone Quality: Low-fidelity microphones or distance from the sound source lead to missing frequencies, which lowers recognition accuracy.
Overlapping Speech: When multiple people talk over each other in a meeting or group setting, it becomes challenging to separate and track individual speakers.

## Slide 13: 2. Linguistic Complexity
Homophones and Ambiguity: Words that sound identical but have different spellings and meanings require the system to use surrounding words (context) to choose the correct one.
Domain Specificity: Medical, legal, or technical terminology often lacks representation in standard training datasets, leading to misheard or phonetically garbled text.
Natural Disfluencies: Conversational speech includes filler words (e.g., "um," "ah"), false starts, and repetitions, which require logic to filter out without delaying the live text output.

## Slide 14: 3. Speaker Diversity and Atypical Speech
Accents and Dialects: Models predominantly trained on mainstream dialects often underperform when processing regional accents or non-native speakers.
Speech Disorders: Atypical speech patterns, such as those caused by dysarthria, aphasia, or apraxia, are frequently misunderstood by standard models due to a lack of diverse training data.

## Slide 15: Light and the Electromagnetic Spectrum

## Slide 16: Speech Acquisition

## Slide 17: Sampling

## Slide 18: Sampling & Quantization

## Slide 19: Image acquisition: camera

## Slide 20: Digital Sampling
Sampling is dictated by the Nyquist sampling theorem which states how quickly samples must be taken to ensure an accurate representation of the analog signal.
The Nyquist sampling theorem states that the sampling frequency must be two times greater than the highest frequency in the original analog signal.

## Slide 22: Speech Visualization

## Slide 23: Features
Zero-crossing
Energy & Power
Fourier descriptors
Formant Frequencies
Mel-frequency cepstral coefficients (MFCC)
LPC

## Slide 24: Zero-crossing

## Slide 25: Energy & Power

## Slide 26: Fourier Descriptors

## Slide 27
DFT

## Slide 28: Rectangle Windowing

## Slide 29: Triangular Weighting

## Slide 30: Hanning Weighting

## Slide 31: Hamming Weighting

## Slide 32: Non Overlapped Windowing

## Slide 33: Overlapped Windowing

## Slide 34: Speech Production

## Slide 35: Speech Production

## Slide 36: Formant Computation

## Slide 37: Cylindrical Vocal Tract Model

## Slide 38: Formant Frequencies

## Slide 39: The Feature Space

## Slide 41: Formant Estimation

## Slide 42: Cepstrum
Compute the real cepstrum of a time-domain signal by calculating the Discrete Fourier Transform (DFT), taking the natural logarithm of its magnitude, and applying an Inverse DFT.
The resulting x-axis is in quefrency (a measure of time) instead of frequency, revealing periodicities in the original spectrum.
The Mathematical Formula

## Slide 43: Step-by-Step Computational Process

## Slide 44: The Cepstrum

## Slide 46: Mel-frequency cepstral coefficients (MFCC)

## Slide 47: Linear Predictive Coding LPC

## Slide 48: The System Models

## Slide 49: The error e(n)

## Slide 50: Autocorrelation Method

## Slide 51: Covariance Method

## Slide 52: Vector Quantization VQ

## Slide 53: The basic block diagram

## Slide 54: The extended block diagram

## Slide 55: Speech Recognition

## Slide 56: Hidden Markov Model
Similar to a markov model except the states are hidden
We now have observations tied to the individual states
We no longer know the exact state sequence given the data
Allows for the modeling of an underlying unobservable process

## Slide 57: HMMs for ASR
First we build an HMM for each phone
Next we combine the phone models based on the pronunciation model to create word level models
Finally, the word level models are combined based on the language model
We now have a giant network with potentially thousands or even millions of states