## Slide 1
Spatial Filtering and Image Enhancement
A comprehensive study of spatial domain enhancements, neighborhood operations, correlation, convolution, and edge optimization.
By Ahmed Yousry Abdelstar Zaalook
Grand Institute for Practical Application
Slide 1

## Slide 2
Fundamentals of Spatial Domain Enhancements
Slide 2
Spatial filtering modifies an image by directly manipulating the intensity of pixels within a local neighborhood.
High Frequencies: Represent rapid variations in brightness (e.g., crisp details, texture transitions, and sharp edges).
Low Frequencies: Capture gradual variations in light intensity (e.g., broad gradients and background shapes).
Filters in Image Processing

## Slide 3
Spatial filters use a convolution matrix (kernel) applied over a neighborhood. The center of the filter corresponds to the target output pixel.
Mathematical Foundations
Slide 3
Filter Kernel
A small coefficient matrix (e.g., 3x3, 5x5) that slides across the pixels to perform neighborhood calculations.
2D Convolution Equation
Where f is the original image, g is the kernel, and j are target coordinates.
Edge Conditions
When processing border pixels, spatial coordinates extend outside the image. Solved via zero-padding, mirroring, or clipping.
Fundamentals of Spatial Filtering
Zero padding adds a border of black pixels (0 value) around the image, mirroring reflects the edge pixels outward to create a symmetrical border, and clipping chops off the boundary pixels entirely so no extra padding is needed

## Slide 4
Though functionally similar, correlation and convolution handle kernel orientation differently, which is mathematically vital.
Mathematical Filtering Differences
Slide 4
Correlation
Correlation moves the filter mask directly over the image and computes the sum of products at each location. It is widely used for template matching and feature finding.
Convolution
Convolution rotates the filter mask by 180 degrees (both horizontally and vertically) before applying the sum of products. It is commutative and mathematically associative.
Correlation vs. Convolution

## Slide 5
Low-Pass Smoothing Operations
Slide 5
Linear spatial filters compute output pixels using weighted linear combinations of neighborhood pixel values. They are excellent for low-pass smoothing.
Box / Average Filter: Simple averaging filter. Replaces target pixel with the mean of its neighbors. Blurs rapid transitions and edges aggressively.
Gaussian Filter: Uses a 2D Gaussian function to assign weights based on distance, preserving details better than simple box blurs.
Linear Filters: Box vs. Gaussian

## Slide 6
Non-Linear Noise Mitigation
Slide 7
Non-linear spatial filters do not use a weighted sum. They rank order neighborhood pixels to compute output values.
Median Filter: Replaces target pixel with the median of neighborhood values. Excellent for removing bipolar (salt-and-pepper) noise without blurring edges.
Max & Min Filters: Max filter replaces pixels with the local maximum (eliminates pepper noise). Min filter replaces with local minimum (eliminates salt noise).
Midpoint Filter: Computes the average of maximum and minimum neighborhood values. Ideal for handling uniform or Gaussian noise.
Non-Linear Order Statistics

## Slide 7
Different noise types demand customized averaging methods. These mathematical variations target specific pixel aberrations.
Specialized Image Restoration Means
Slide 8
Arithmetic Mean
Standard pixel averaging. Smoothes local noise variations but blurs boundaries.
Geometric Mean
Multiplies neighborhood pixels to the power of 1/mn. Retains image details better than arithmetic.
Harmonic Mean
Excellent for removing salt noise. Struggles with pepper noise.
Contra-Harmonic
Parameterized by power Q. Removes salt noise (Q < 0) or pepper noise (Q > 0).
Non-Linear Restoration: Mean Filters

## Slide 8
Image sharpening highlights boundaries and transitions. This domain operation is achieved through discrete calculus (differentiation).
Calculus of Image Sharpening
Slide 9
Gradient Detection
Calculates differences in adjacent intensity. Produces wider edges and responds strongly to step-like transitions.
Acceleration Detection
Calculates rate of change of differences. Yields finer edge lines, responds strongly to details, and crosses zero at transitions.
Enhancement & Derivatives

## Slide 9
Isotropic Edge Optimization
Slide 10
The Laplacian is a rotation-independent, second-order derivative operator used for isotropic edge enhancement.
Standard 3x3 Laplacian Matrix
0 | 1 | 0
1 | -4 | 1
0 | 1 | 0
Center coefficient has opposite sign of outer coefficients. Reverses local gradients to accentuate edge differences.
Discrete Form: Sums the second derivatives in both principal spatial axes.
Sharpening Blend: Sharpens the original image by adding or subtracting the Laplacian:
The Laplacian Sharpening Operator

## Slide 10
Unsharp masking extracts detailed edge masks by subtracting smoothed images, combining them with the original:
Traditional Image Sharpening Workflows
Slide 11
STEP 1
Smooth Image
Create a blurred version of the original image.
STEP 2
Compute Mask
Subtract the blurred version from the original.
STEP 3
Scale Margin
Configure weight to control sharpness intensity.
STEP 4
Final Blend
Add the scaled mask back onto the original frame.
Unsharp Masking Workflow

## Slide 11
https://www.dynamsoft.com/blog/assets/images/uploads/2019/07/figure-231.png
Source: www.dynamsoft.com
https://bartwronski.com/wp-content/uploads/2020/02/shapes-mid-rank.png
Source: bartwronski.com
https://media.geeksforgeeks.org/wp-content/uploads/20221119120356/Themechanicsofspatialfilteringusinga33filtermask.png
Source: www.geeksforgeeks.org
Image Sources